## Slide 1: FROGGER! (on Spartan 3-E Dev. Board)
ECE 525.442 VHDL Microprocessor Design
Final Student Project
August 14th, 2012
Emily Kan
Erik Lee
Edward Jones

## Slide 2: Outline
Introduction
Background
Design
Implementation/ Verification
  Troubleshooting
Results & Analysis
Conclusion
  Future Outlook
References
*Note: Not our version implemented in this project!

## Slide 3: Introduction
Low-cost / scalable design influence increases with advances in modern technology
Design reusability becoming more prominent in marketplace
Digital Design w/FPGAs begins to grow
  Core IP VHDL files easily adaptable and reusable with existing FPGAs
  Multiple VHDL core instantiations leads to improved design flow

## Slide 4: Introduction cont’d
Video game development becomes easier!
  Functionality of video games application is moved from circuit board ICs to FPGA
    Alleviates some design challenges, leaving designers to create the implementation
      Keyboard use
      Port Control
      Display output
      FPGA selection

## Slide 5: Background
Flow of game design
Initialize VGA Controller
Create initial Background Display
Generate Moving Objects
Create Frog at Reset Position
Detect Frog Motion
Check Frog position against objects
Output Score
Start-Up Sequence
Game Sequence

## Slide 6: Design
Four files for initial Start-Up Sequence
  (1) vgaSyncGenerator.vhd
  (2) backGroundGenerator.vhd
  (3) Objects.vhd
  (4) randomGenerator.vhd
Entity definitions for VHDL files

## Slide 7: Design cont’d
vgaSyncGenerator.vhd
  Creates Horizontal & Vertical display using pixel counters: Hsync / Vsync driven by a 25 MHz clock generated from FPGA
  Color output created by 8-bit colors generated on VGA port
640
480
Control Module
H-sync
V-sync
Red (3-bit)
Green (3-bit)
Blue (2-bit)
VGA Port
Output Resolution

## Slide 8: Design cont’d
backGroundGenerator.vhd
  Creates the initial background image as a “map” for the game
  Colors created from horizontal and vertical counting vector position from VGA driver signals
Upper Half depicts “water” zone
Lower Half depicts “street” zone
Grass area always “safe”

## Slide 9: Design cont’d
backGroundGenerator.vhd
  Creates the initial background image as a “map” for the game
  Colors created from horizontal and vertical counting vector position from VGA driver signals
Upper Half depicts “water” zone
Lower Half depicts “street” zone
Grass area always “safe”

## Slide 10: Design cont’d
randomGenerator.vhd
  Implements a random stream of bits
    Implements a 12 bit Linear Feedback Shift Register ( Taps: 12, 6, 4, 1 )
    Independent reset
    Also includes an input from the user to make numbers more random
    Length, color, and jump are influenced by the random generator

## Slide 11: Design cont’d
Four files for Game Sequence
  (1) frogGenerator.vhd
  (2) frogLocation.vhd
  (3) collisionDetection.vhd
  (4) score.vhd
Entity definitions for VHDL files

## Slide 12: Design cont’d
frogGenerator.vhd
  Generates a square block dubbed as the “frog” to traverse through generated course
  Implements “dead frog” flashing code if frog moves into hazardous play field
Normal Frog Color
Dead Frog Flashing

## Slide 13: Design cont’d
frogLocation.vhd
  As the frog moves up the screen, row position & column position vs. objects is being tracked for collision detection
Column Position (640 Pixels)
Row position
(15 blocks)

## Slide 14: Design cont’d
collisionDetection.vhd
  Mealy State machine
    Places frog “block” in action state
      Five states as frog travels through game map
        On Road
        On Grass
        On River
        Dead
        Win
State changes depending on object and background colors

## Slide 15: Design cont’d
On Grass
On Road
Dead
Win
All Bgcolor=black
Dead=‘0’
All Bgcolor=green/
Dead=‘0’
Any Objcolor /= black
Dead =‘0’
Counter< 3secs
Dead=‘1’
Counter >=3secs
Dead=‘0’
Reset=‘1’
All objcolor = black
Dead = ‘0’
All Bgcolor=blue
Dead=‘0’
Any objcolor = green Row = 0
Dead=‘0’
Counter< 3secs
Dead=‘0’
On River
Any objcolor = brown/
OnLog =‘1’
Any Bgcolor = black
Dead=‘0’
All
Bgcolor=green
Dead=‘0’
Counter>=3secs/
Reset=‘1’, Win=‘1’
collisionDetection.vhd cont’d…

## Slide 16: Design cont’d
Score.vhd
  Point value of 10, 20, or 50 points depending on level of difficulty
    Difficulty set by user (3 settings)
    Max of 5000
    Can only set at start position
  Output of running total is displayed on seven segment display on Spartan 3E dev board

## Slide 17: Design cont’d
Miscellaneous Components
  Keyboard Component Instantiation
    Core Implemented in design
    Mapped to frog direction
      Output clock to keyboard
      Input Key Press data from keyboard
      Map data to frog direction
  De-bounce Circuit
    Mapped to buttons on FPGA
    for user input and switches for levels
Up | Down | Left | Right
Game Module |  |  | 
Keyboard
Data
Clock
PS/2 Module
Data
Clock

## Slide 18: Design cont’d
User input to game
  Choice of keyboard entry or development board

## Slide 19: Implementation & Verification
Synthesized Top Module
  15 inputs, 21 outputs
Troubleshooting
  Object verification, death sequence

## Slide 20: Results & Analysis
VGA drivers
    2 Counters ( pixel count)
    35 DFFs
    2 Adders / Subtractors
    8 Comparators
Frogger Keyboard driver
    1 Counter
    20 DFFs
    1 XOR
Background Generator
    8 DFFs
Object Generator
    60 DFFs
    7 Adder / Subtractor
    9 Comparators
Random Generator
    1 Counter
    1 DFF
    1 Comparator
    1 Xor
Frog Generator
    1 Counter
    8 DFFs
    5 Comparators
Frog Location
    1 ROM (frog Row location)
    42 DFFs
    3 Adders / Subtractors
    3 Comparators
1 Finite State Machine
    5 states, 61 transitions, 22 inputs, 3 outputs
    1 Counter
    64 DFFs
    8 Comparators
Score Keeper
    1 ROM
    38 DFFs
    1 Adder/Subtractor
    1 Comparator

## Slide 21: Results & Analysis
7 Segment Driver
    1 ROM
    1 Counter
    34 Adders / Subtractors
    34 Comparators
    4 Multiplexers
LED Decoder
    1 ROM
Top Level Frogger
    1 Counter
    9 DFFs
    1 Comparator

## Slide 22: Results & Analysis cont’d
FPGA Resource Utilization
HDL Resource Synthesis Report | 
ROMs | 4
Adders/Subtractors | 124
Counters | 16
Accumulators | 48
Registers | 533
Comparators | 178
Multiplexors | 1
FSMs | 1
XORs | 57
Flip Flops | 1163
Inputs | 15
Outputs | 21

## Slide 23: Results & Analysis cont’d
FPGA Device Utilization

## Slide 24: Conclusion
Frogger game provided in-depth experience into all phases of design and development using Xilinx FPGA tools:
    Multiple Component Instantiation
    Multi-file Design Integration
    I/O Port configuration
Spartan 3E development board package provides robust environment for video game creation:
    Map drawing and level selection
    Character direction and event driven outcomes
    Score computation

## Slide 25: Conclusion cont’d
Future Outlook / Development
  Development of frog and background objects using image files pre-loaded into SRAM
  Reduction of device utilization
    Use block or distributed RAM
    Reduce number of DFFs
    Use an embedded processor to reduce the duplicated logic
  Add levels of complexity
    Additional frog lives
    “Win” screen
    Sound effects

## Slide 26: References
NEXYS2 Reference Manual
FPGA Resource Guide http://www.digilentinc.com/showcase/contests/designcontest.cfm?contestid=8
Keyboard Implementation & Application http://www.pyroelectro.com/tutorials/ps2_keyboard_interface/theory_ps2.html