## Slide 1: FROGGER! (on Spartan 3-E Dev. Board)
ECE 525.442 VHDL Microprocessor Design
Final Student Project
August 14th, 2012
Emily Kan
Erik Lee
Edward Jones

## Slide 2: Outline
Introduction
Background
Design
Implementation/ Verification
Results & Analysis
Conclusion
  Troubleshooting
  Future Outlook
References
*Note: Not our version implemented in this project!

## Slide 3: Introduction
Low-cost / scalable design influence increases with advances in modern technology
Design reusability becoming more prominent in marketplace
Digital Design w/FPGAs begins to grow
  Core IP VHDL files easily adaptable and reusable with existing FPGAs
  Multiple VHDL core instantiations leads to improved design flow

## Slide 4: Introduction cont’d
Video game development becomes easier!
  Functionality of video games application is moved from circuit board ICs to FPGA
    Alleviates some design challenges, leaving designers to create the implementation
      Keyboard use
      Port Control
      Display output
      FPGA selection

## Slide 5: Background
Flow of game design
Initialize VGA Controller
Create initial Background Display
Generate Moving Objects
Create Frog at Reset Position
Detect Frog Motion
Check Frog position against objects
Output Score
Start-Up Sequence
Game Sequence

## Slide 6: Design
Three files for initial Start-Up Sequence
  (1) vgaSyncGenerator.vhd
  (2) backGroundGenerator.vhd
  (3) Objects.vhd
Entity definitions for VHDL files

## Slide 7: Design cont’d
vgaSyncGenerator.vhd
  Creates Horizontal & Vertical display using count pixel position with H / Vsync driven by a 25 MHz clock generated from FPGA
  Color output created by 8-bit colors generated on VGA port
640
480
Control Module
H-sync
V-sync
Red (3-bit)
Green (3-bit)
Blue (2-bit)
VGA Port
Output Resolution

## Slide 8: Design cont’d
backGroundGenerator.vhd
  Creates the initial background image as a “map” for the game
    Colors created from horizontal and vertical counting vector position from file vgaSyncControler.vhd
Upper Half depicts “water” zone
Lower Half depicts “street” zone
Grass area always “safe”

## Slide 9: Design cont’d
Objects.vhd
  Implements moving objects for frog to traverse through
    Upper portion of screen, water collision results in death
    Lower portion of screen, object collision results in death
Log objects on blue portion, car object on black portion

## Slide 10: Design cont’d
Four files for Game Sequence
  (1) frogGenerator.vhd
  (2) frogLocation.vhd
  (3) collisionDetection.vhd
  (4) score.vhd
Entity definitions for VHDL files

## Slide 11: Design cont’d
frogGenerator.vhd
  Generates a square block dubbed as the “frog” to traverse through generated course
  Implements “dead frog” flashing code if frog moves into hazardous play field
Normal Frog Color
Dead Frog Flashing

## Slide 12: Design cont’d
frogLocation.vhd
  As the frog moves up the screen, row position & column position vs. objects is being tracked for collision detection
Column Position (640 Pixels)
Row position
(16 blocks)

## Slide 13: Design cont’d
collisionDetection.vhd
  Mealy State machine
    Places frog “block” in action state
      Five states as frog travels through game map
        On Road
        On Grass
        On River
        Dead
        Win
State changes depending on frog location

## Slide 14: Design cont’d
On Grass
On Road
Dead
Win
All Bgcolor=black
Dead=‘0’
All Bgcolor=green/
Dead=‘0’
Any Objcolor /= black
Dead =‘0’
Counter< 3secs
Dead=‘1’
Counter >=3secs
Dead=‘0’
Reset=‘1’
All objcolor = black
Dead = ‘0’
All Bgcolor=blue
Dead=‘0’
Any objcolor = green Row = 0
Dead=‘0’
Counter< 3secs
win=‘1’
On River
Any objcolor = brown/
OnLog =‘1’
Any Bgcolor = black
Dead=‘0’
All
Bgcolor=green
Dead=‘0’
Counter>=3secs/
Reset=‘1’
collisionDetection.vhd cont’d…

## Slide 15: Design cont’d
Score.vhd
  Upon successfully reaching the end of the course, the user is awarded 10, 20, or 30 points depending on level of difficulty
    Difficulty set by user (3 settings)
  Output of running total is displayed on seven segment display on Spartan 3E dev board
    Utilizes seg7driver.vhd, counterwithPulse.vhd, and led_decoder.vhd

## Slide 16: Design cont’d
Miscellaneous Components
  Keyboard Component Instantiation
    Core Implemented in design
    Mapped to frog direction
      Output clock to keyboard
      Input Key Press data from keyboard
      Map data to frog direction
  De-bounce Circuit
    Mapped to buttons on FPGA
    for user input and switches for levels
Up | Down | Left | Right
Game Module |  |  | 
Keyboard
Data
Clock
PS/2 Module
Data
Clock

## Slide 17: Design Cont’d
User input to game
  Choice of keyboard entry or development board

## Slide 18: Implementation & Verification
VGA drivers
  2 Counters ( pixel count)
  35 DFFs
  2 Adders/Subtractors
  8 Comparators
PS/2 Keyboard driver
  1 Counter
  20 DFFs
  1 Xor
Background Generator
  8 DFFs
Object Generator
  2 Accumulators
  8 DFFs
  1 Adder/Subtractor
  5 Comparators
Frog Generator
  1 Counter
  8 DFFs
  5 Comparators
Frog Location
  1 ROM (frog Row location)
  42 DFFs
  3 Adders/Subtractors
  5 Comparators
1 Finite State Machine
  5 states, 61 transitions, 22 inputs, 3 outputs
  1 Counter
  64 DFFs
  8 Comparators

## Slide 19: Results & Analysis
FPGA Resource Utilization
Resource Synthesis Summary | 
ROMs | 4
Adders/Subtractors | 64
Counters | 15
Accumulators | 48
Registers | 97
Comparators | 191
Multiplexors | 1
FSMs | 1
XORs | 8
Flip Flops | 1024
Inputs | 15
Outputs | 10

## Slide 20: Results & Analysis cont’d
FPGA Device Utilization

## Slide 21: Conclusion
Frogger game provided in-depth experience into all phases of design and development using Xilinx FPGA tools:
    Multiple Component Instantiation
    Multi-file Design Integration
    I/O Port configuration
Spartan 3E development board package provides robust environment for video game creation:
    Map drawing and level selection
    Character direction and event driven outcomes
    Score computation

## Slide 22: Conclusion cont’d
Troubleshooting
  ??????
Future Outlook / Development
  Development of frog and background objects using image files pre-loaded into SRAM
  Modified level designs

## Slide 23: References
NEXYS2 Reference Manual
FPGA Resource Guide http://www.digilentinc.com/showcase/contests/designcontest.cfm?contestid=8
Keyboard Implementation & Application http://www.pyroelectro.com/tutorials/ps2_keyboard_interface/theory_ps2.html

## Slide 24: Design Rules Implementation
Finite State Machine - Mealy
Define outputs
  Dead
  Reset
  On a log
Define inputs
  Object colors
  Background colors
  Frog position
Define states
Define transitions (interactions with objects and background)
Notes: Finite State Machine – 5 states
Define Outputs:
Flag when frog is hit by a car
Flag when frog is on a log
Flag for resetting frog back to homebase
Define Inputs:
4 corners of frog (xy-pixel)
Object color
Background color
Frog Position
Define states:
5 states – onGrass, onRoad, onRiver, Dead, Win
Transitions